Hacking binaries
reverse engineering binaries
cracking applications

---
Binary
- Code that is compiled to run with a particular processor
- Binary contains machine code
- Machine code is the language of the processor
- Windows executable .exe, Linux ELF
- Written in some language (C, C++)
- Compiled to machine language → binary file
- Java is compiled into byte code for the JVM
- binary = native code = machine code = executable

---
High level code
(Java)
High level code
(C)
compiler
Byte code
compiler
JVM
Machine code
(binary)
Machine code
(binary)

---
Hacking a binary
- Change the binary in such a way that it behaves differently
- E.g.
  - Modifying an application so it won’t send your personal data to the company
  - Removing protections from malware so it can be analysed
  - Modifying an application to make it ‘registered’ (crack)

---
Understand the binary
- We only have the binary with unreadable machine code
- Make it more human readable
- Decompile:
  - high level code machine code
  - high level code machine code (difficult)
  - Large applications really difficult or impossible.
- Disassemble:
  - No lost information but difficult to understand
  - We get disassembly code (instructions), x86
  - ASM is the language of the CPU

---
Now some low level stuff...

---
CPU
- Executes CPU instructions, machine code
- Registers = super fast memory inside the CPU
  - Used to store variables; ~200x faster than RAM
  - 64bits
  - rax, rdi, ecx, dil
- FLAGS register used to hold state
  - Some instruction modifies register and next instruction uses state of register
  - Used with conditional jumps, JA, JNE, Jxx
  - ZF; 0 or 1
  - CF; 0 or 1

---
ASM CPU instructions
mov A, B = copy B to A
cmp A, B = compare A to B (substract B from A)
jmp [Address] = continue execution from [Address]
ja [Address] = Jump Above. Conditional. Only jump if certain flags are set. Many Jxx, jne, je, jle,…
ZF = Zero Flag. Will be set when the result of a cmp is zero. Just a bit that can be set in the processor
call = call function and return value in rax

---
if/else in ASM
if (a == 1) {
printf()
} else {
atoi()
}
0x01 cmp ecx, 1 (ZF set)
0x02 je 0x27
0x03 call atoi
…
0x27 call printf

---
Example application
- Change it’s behaviour so that it’s registered
- Runs in some state
  - State: not registered (“evaluation”)
  - We want: registered
- How do we get to the registered state?
- How did the high level code look like?

---
Registration logic
- How would the application check if it’s registered?
- At some point, there must be function checking if the program is registered (check)
  - Could be many checks
  - We don’t know how it looks like
- Find that registration-check function (routine)

---
Find the registration routine
- Can be anywhere in the many lines of assembly
- Hypothesis:
  if ( !isRegistered() ) {
    …
    printString(“evaluation”);
  } else {
    ...
    printString(“string_we_dont_know”)
  }

---
Flow that leads to “evaluation”
Print “evaluation” in the title bar
If ( !isRegistered() )
Else { }
Print something else in the title bar
Find where “evaluation copy” is used
code path
code path

---
Attack plan
- Search for the “evaluation copy” string in the binary
- Trace back to find the registration routine
- Modify registration routine so it takes the ‘else’

---
x64dbg
- Disassembler: human readable machine code (ASM)
- Debugger:
  - Pause execution of code
  - Read contents of registers and other CPU information

---
demo

---
Protecting
- Obfuscate
- Pack
- VM
- Online verfication